## Slide 2
Schematic of the “Flamethrower”
Simpler manufacturing than the Mayon Turbo Stove
Fuel intake on one side only
Ash is collected on the same side
smokestack
fuel hopper
ash collector
air intake

## Slide 3
Schematic of the “Flamethrower”
Simpler manufacturing than the Mayon Turbo Stove
Fuel intake on one side only
Ash is collected on the same side
rice hulls
twin pipes
perforated aluminum sheet metal

## Slide 4
How Rice Hull Combustion Works
Initial kindling or fire starter necessary
Rice hulls outgas between 200-450°C (392-842°F)1
  Below 200°C, negligible decomposition
  At 200°C, darkish yellow
  At 450°C, >90% of volatile matter separates
Proper fuel-to-air mixture sustains the burn
1 M.A. Hamad. “Thermal Characteristics of Rice Hulls.” 28 January 1981.

## Slide 5
Removing Hazardous Smoke
Rice hull ash and smoke contain silica, SiO2
  Same material as sand
  Need to prevent inhalation of smoke
Exhaust system to redirect any smoke
The smokestack was effective, and the only smoke came out of the top
Next design needs to ensure good air quality

## Slide 6
Getting Rid of the Ash
Tap the side of the stove, gravity will cause more fuel to feed in and the ash will fall into the ash collector
For ease of use, the ash collector and fuel feed are facing the same side of the stove

## Slide 7
Ideal Air Flow
Air flows through the fuel, combines with the outgas, and combusts
Convection draws the hot air upward to the stovepipe, which draws more air through the intake to balance the pressures

## Slide 8
Actual Observed Air Flow
Air preferentially flows around the rice hull tray
Not enough air gets to the rice hulls to sustain a clean burn
The rice hulls simply smolder and produce a lot of smoke

## Slide 9: Redesign Considerations
Air will flow in path of least resistance
Maximize amount of useful air to the rice hulls
Block areas where non-useful air can flow
Effective method for removing ash
Ability to CONTROL the fuel and/or air
Air and heat flow through rice hulls is difficult
  The thermal resistance R-value for rice hulls is about 3.0 per inch, good for insulation2
2 P. A. Olivier. “The Rice Hull House.” 2004.